## Slide 1: ARM - 5 Marks Theory
Vraj Suratwala

## Slide 2: Introduction
ARM (Advanced RISC Machine) is a family of 32-bit RISC processor cores designed mainly for embedded and low-power applications.
ARM cores are known for high performance, low power consumption and low system cost. ARM Ltd designs and licenses ARM processor cores to semiconductor manufacturers rather than manufacturing the chips itself.
1. RISC Architecture
ARM follows the RISC (Reduced Instruction Set Computer) architecture. It uses a relatively simple instruction set and is designed for efficient and fast execution. ARM is mainly used in embedded systems, mobile devices, automotive, industrial and networking applications.

## Slide 3: Components
2. Registers
  ARM has 37 registers, each 32 bits wide:
  30 General-purpose registers
  1 Program Counter (PC)
  1 Current Program Status Register (CPSR)
  5 Saved Program Status Registers (SPSR)
  The registers are organized into different banks, and the accessible bank depends on the processor's current mode
3. Pipeline
ARM uses an instruction pipeline to improve execution speed. In the basic ARM core shown in the PPT, the pipeline has three stages:
Fetch → Decode → Execute
While one instruction is being executed, another can be decoded and another fetched, allowing multiple operations to occur simultaneously.

## Slide 4: Components
4. Load/Store Architecture
ARM uses a Von Neumann load/store architecture. Memory is accessed mainly through load and store instructions, while arithmetic and logical operations are performed on registers. It has a 32-bit address space and supports 8-bit bytes, 16-bit half-words and 32-bit words.
5. ARM and Thumb States
ARM supports different execution states. In ARM state, instructions are 32 bits wide, while in Thumb state, instructions are 16 bits wide. Thumb provides better code density and is useful when memory is limited. The processor can switch between ARM and Thumb states using the BX instruction.
6. Barrel Shifter
A special feature of ARM is its barrel shifter, which allows shifting or rotating an operand as part of another instruction. It supports operations such as LSL, LSR, ASR, ROR and RRX. This helps ARM perform efficient arithmetic and logical operations.

## Slide 5: Simple ARM Flow
ARM PROCESSOR
↓
Fetch Instruction
↓
Decode
↓
Read Registers
↓
Barrel Shifter
↓
ALU Operation
↓
Write Back Result
↓
Next Instruction