## Slide 1: Sensors & Actuators
IoT
Vraj Suratwala

## Slide 2: Introduction to Sensors
A sensor is a device that detects changes in the physical environment and converts them into signals that electronic systems can process.
1. Detection
2. Conversion
3. Transmission

## Slide 3: Ultrasonic Sensors
An ultrasonic sensor is a device used to measure the distance between the sensor and an object using ultrasonic sound waves.
It sends a sound wave at a specific frequency toward an object. When the wave hits the object, it reflects back (echoes) to the sensor. The distance is calculated using the time taken by the sound wave to return.
The ultrasonic sensor works on the Echo / Time-of-Flight principle.
Basic principle:
Transmit → Sound travels → Hits object → Reflects → Echo received → Time measured → Distance calculated
The sensor emits an ultrasonic wave, typically around 40,000 Hz (40 kHz). If an obstacle is present in its path, the wave is reflected back toward the sensor. The sensor measures the travel time of this reflected wave

## Slide 4: Diagram

## Slide 5: Distance Calculation

## Slide 6: Configuration

## Slide 8: Advantages
It can measure the distance to an object without physical contact.
It uses sound waves rather than visible light.
It can detect objects/obstacles in its path.
The distance can be calculated from the measured echo time.

## Slide 9: LDR (Light Dependent Resistor)
LDR (Light Dependent Resistor) is a light-sensitive resistor whose resistance changes according to the intensity of light falling on it.
For the most common type of LDR:
More light → Lower resistance
Less light / darkness → Higher resistance
Therefore, LDRs are used in light-sensing circuits.

## Slide 10: Working

## Slide 12: Construction
The PPT describes the manufacture of a cadmium sulfide (CdS) LDR.
Highly purified cadmium sulfide powder is mixed with inert binding materials.
The mixture is pressed and sintered.
Electrodes are vacuum evaporated onto the surface.
The electrodes form interleaving comb-like structures.
Connection leads are attached.
The disc is mounted inside a glass envelope or encapsulated in transparent plastic to prevent surface contamination.
The spectral response of CdS matches that of the human eye.

## Slide 13: Application
The PPT specifically states that LDRs are used in light-sensing circuits.
Examples of light-sensing applications include:
Automatic light control
Light/dark detection
Automatic street-light systems
Light intensity sensing

## Slide 14: Graph

## Slide 15: Diagram

## Slide 16: Infrared (IR) Sensor
An Infrared (IR) sensor is a sensor that uses infrared light to detect objects. It uses a light source, typically an IR LED, and a light-sensitive device such as a photodiode or phototransistor to detect the reflected IR ligh

## Slide 17: Working Steps
1. IR emission:
  An IR LED emits infrared light at a particular wavelength.
2. Light falls on object:
  The emitted IR light travels toward the object.
3. Reflection:
  If an object is close to the sensor, the IR light bounces/refects from the object.
4. Light detection:
  The reflected light reaches the photodiode or phototransistor.
5. Intensity change:
  The received light intensity increases significantly.
6. Object detection:
  This change can be detected using a threshold, allowing the system to determine whether an object is present.

## Slide 20: Working

## Slide 21: Thermistors
A thermistor is a type of resistor used to measure temperature changes. Its resistance changes when the temperature changes.
THERMal + resISTOR = THERMISTOR

## Slide 22: Types of Thermistor
1. PTC – Positive Temperature Coefficient
For a PTC thermistor:
Temperature ↑ → Resistance ↑
If k is positive, resistance increases as temperature increases.
It is also called a Posistor.
2. NTC – Negative Temperature Coefficient
For an NTC thermistor:
Temperature ↑ → Resistance ↓
If k is negative, resistance decreases as temperature increases.

## Slide 23: Comparision

## Slide 24: Explaination

## Slide 25: Humidity Sensor
A humidity sensor, also called a hygrometer, is a device used to sense, measure, and report the relative humidity of air.
Humidity represents the amount of moisture present in the air. Relative humidity is the ratio of the actual moisture in the air to the maximum amount of moisture that the air can hold at that temperature.
Classification of Humidity Sensors
A. Based on type of humidity measuredNAbsolute Humidity (AH) Sensor
  Relative Humidity (RH) Sensor
B. Based on the parameter used for measurement
  Capacitive Humidity Sensor
  Electrical Conductivity / Resistive Humidity Sensor
  Thermal Conductivity Humidity Sensor

## Slide 26: Relative Humidity
Relative Humidity (RH) indicates how much moisture is present in the air compared with the maximum moisture that the air can hold at that temperature.
It is commonly expressed as a percentage (%).
For example:
50% RH means the air contains approximately half of the moisture it could hold at that temperature.

## Slide 27: Capasitive Humidity Sensor
A capacitive humidity sensor is a type of humidity sensor that works using the capacitive effect.
In a capacitive RH sensor, the electrical permittivity of the dielectric material changes when humidity changes.
Key Point
Humidity changes → Dielectric permittivity changes → Capacitance changes → Humidity detected

## Slide 29: Construction
Two metal electrodes are deposited on the substrate.
The electrodes can be made from aluminium, platinum, or chromium.
The electrodes form an interdigitized pattern.
A dielectric layer is deposited over the electrodes.
Two temperature-sensitive resistors may also be placed on the same substrate for temperature compensation
Advantages of Capacitive Humidity Sensors
According to the PPT, capacitive humidity sensors are useful when factors such as:
Cost
Rigidity
Size

## Slide 30: Diargarm

## Slide 31: DHT11 / DHT22 Temperature & Humidity Sensor
DHT11 is a basic, low-cost digital temperature and humidity sensor.
It uses:
  A capacitive humidity sensor to measure humidity
  A thermistor to measure temperature
  An internal IC to process the measurements
  The output is provided as a digital signal, so an analog input pin is not required.

## Slide 35: IMP

## Slide 36: Thank you
Vraj Suratwala
Department of ICT, VNSGU